## Slide 1
LAN and Local device management
IETF SNMP + DMTF DMI
Overview and Extension to multifunction devices
Tom Hastings
Xerox Corporation

## Slide 2
Agenda
Status of SNMP, DMI, Printer MIB, Printer MIF standards
Overview of IETF SNMP and MIBs
  remote management on a LAN
Overview of DMTF DMI and MIFs
  local management on a PC
Steps for Extension to multifunction

## Slide 3
Status of SNMP, Printer MIB standards
SNMPv1 internet standard 1988
SNMPv2 approved, except for security
Printer MIB, RFC 1759, March 1994
  is a proposed standard - at least 6 months
  next step is a draft standard - at least 3 months
  approved standard
  available: ftp.isi.edu /in-notes/rfc1759.txt

## Slide 4
Status of DMTF, Printer MIB standards
Desktop Management Task Force (DMTF)
  consortiium: DEC, HP, IBM, Intel, Microsoft, Novell, SunConnect, SynOptics
DMTF DMI V1.0 standard published April 1994
Printer MIF, WG draft September 1995
Printer WG (PWG), joint IETF/DMTF, started Sept 1993

## Slide 5
Overview of IETF SNMP
Simple Network Management Protocol
for managing devices and services
defines set and get functions
on data objects (attributes)
management station issues sets and gets
agent implements the sets and gets for a particular MIB

## Slide 6
Management Information Base (MIB)
need a specification for each kind of device
  Examples: Printer MIB, host resources MIB
specification of data objects (attributes)
  Examples: DeviceType, DeviceModel, InputStatus, InputMediaName, CurrentOperator, ServicePerson, ConsoleDisable,

## Slide 7
Printer MIB, RFC 1759
74 accessible objects in 8 mandatory groups
58 accessible objects in 10 optional groups
requires Host Resouces MIB and MIB II
  23 accessible objects in 1 mandatory group
  32 accessible objects in 5 optional groups

## Slide 8
Printer MIB device model

## Slide 9
Printer MIB place in the network

## Slide 10
DMI Architecture
Service Layer
Component Interface
Management Interface
SNMP
Agent
Remote
Agent
Management Applications
Hardware and Software Components
MIF
database
Local
Program
DMI Architecture

## Slide 11
Implementing to the DMI enables management
Remote
Agent
DMI
...
Installation
Programs
Third Party
Applications &
Configuration
Programs
Hardware
Modems,Disk Drives
Video & Network Adapter
Software
OS, Applications,
Drivers, BIOS
Peripherals
Mouse, Printer,
Modems , Tape Drives
SNMP
Agent
CMOL
Agent
RPC
or
NOS
Link
Agents
Providing
Network
Access
Network
Management
Applications
SNMP and
Element
Management
Consoles
Enterprise
Management
Consoles
PC LAN
Management
Platforms
and Services
Diagnostics
and Alerts
Product Setup
and Configuration
N
E
T
W
O
R
K

## Slide 12
Extending the Printer MIB to MF
New MIB for managing scanner devices
New MIB for managing multifunction devices
New MIB for job monitoring
  print jobs
  multifunction jobs

## Slide 13
Need to define scanner and FAX objects
attributes of a scanner device
attributes of a FAX device
define new DPA object classes
like printer object
xxx-supported attributes
xxx-ready attributes
state attributes

## Slide 14
Extension to multifunction
job has source and destinations
source:
  scanner
  fax
  network file system
destinations:
  printer
  fax
  network file system

## Slide 15
Multiple destination jobs
simple for PCs and simple devices
yet extend to high end systems
introduce idea of jobs containing jobs
so each basic job has only one destination type
probably want to allow multiple phone numbers on a single FAX

## Slide 16
Creating multi-level jobs
server does it transparently to client
  client specifies scan source, print destination
  server transforms one-level job into two-level
    job contains one scan job and one print job
client submits multi-level job explicitly
  extend DPA protocol
  add create subjob operation

## Slide 17
Next Steps
need people with MF expertise to define scanner/FAX SNMP device MIBs and DMI MIFs
setup an IETF/DMTF WG to define scanners and FAX SNMP MIBs?
  or join existing IETF/DMTF PWG?
  or join some other group? MFPA WG?
join ISO DPA WG to extend ISO DPA
keep MIB objects equivalent to new DPA job, scanner/FAX device attributes

## Slide 18
More Information on IETF/DMTF PWG
to be added to email list:
pmi-request@hpbs987.boi.hp.com
PWG is meeting monthly

## Slide 19
More Information on DMTF
FaxBACK: (800) 525-3019
  Ask for Document #5572
DMTF hotline: (503) 221-2945
  White papers
  Specifications
  Mailing lists
  Bulletin board
  FTP server
*Other brands and names are the property of their respective owners.